## Slide 1: Heating the Midwest

## Slide 3: Duluth Energy Systems

## Slide 4: Before the Tourists

## Slide 5: Duluth Energy Systems

## Slide 6: Duluth Energy Systems
Duluth Steam 1932 – 1979
  Private Operator
  Lacked financing for new air permit regulations
Duluth Steam Co-Operative 1979-2012
  Completed capital needs
  Low cost but status quo
Ever-Green Energy 2012 – Current
  Manager and Operator
  Strategic Plan
  Rebranded Duluth Energy System 2015

## Slide 7: Duluth Energy Systems
System Service Data:
STEAM
  Four 1932 Edge Moor coal fired boilers
  Two Coal Only (25 MW)
  Two Coal / Gas (28 MW)
  164 Buildings with Steam
  150 psi steam
  10 miles of distribution piping
  Open Loop

## Slide 8: Duluth Energy Systems
System Service Data:
HOT WATER
  Energy supplied primarily by turbine exhaust steam
  6 Buildings (DECC / Amsoil)

## Slide 9: Duluth Energy Systems
System Service Data:
CHILLED WATER
  800 Ton Steam Absorption Chiller
  5 Buildings
  ¾ mile distribution

## Slide 10: Duluth Energy Systems
We provide thermal energy for:
  Hospitals
  Government Buildings
  Financial Institutions
  Hotels
  Small Shops
  Tourist Centers

## Slide 11
Thermal Energy Provider to

## Slide 13: Strategic Plan
Critical Upgrades to Existing System
Efficiency Improvements (Hot Water)
Renewable Energy
System Growth

## Slide 14: Strategic Plan
Critical Upgrades to Existing System
  Total Plant Outage / Repair
  Safety Upgrades
  Equipment Overhaul / Replacements
  Trending & Data
  Gas Burner Management System Upgrade
  Reliable Emergency Power

## Slide 15: Strategic Plan
Efficiency Improvements
  Hot Water Conversion
  How to Fund?
  Where to Start?

## Slide 16: Conversion to Hot Water
Duluth announced intention to modernize Superior Street
17 Blocks over 3 years
Building-Face to Building-Face Project
Replacement and Upgrade of all Utilities

## Slide 17: Superior Street Project
1932

## Slide 18: Decisions…

## Slide 19: Because Compared to Steam…
Hot Water is:

## Slide 20: Steam System Inefficiency
365°
180°
80°
43°

## Slide 21: Hot Water System Efficiency
200°
160°

## Slide 22: Hot Water Benefits
No Manholes!
Up to 20% System Losses

## Slide 23: Superior Street Project
Bonding Request
  2016 request for $21M to support the system transformation (no bonding bill)
  2017 – Awarded $15M in state bonding
  2018 – Request for additional $7M
  Additional funds to come from other sources
  Superior Street load is 30% of system

## Slide 24: Superior Street Phasing

## Slide 25: Superior Street Hot Water Routing

## Slide 26: Strategic Plan
Renewable Energy
Made Possible By:
  Reliable Plant
  Modern Distribution
  Energy Plan
  Forward Thinking (EGE & City)

## Slide 27: Strategic Plan
Renewable Energy
Solid Fuel & Liquid Fuel Options Investigated
Solid Fuel:
  Capital intensive
  Significant space requirements
  Messy process in the heart of the tourist district
RFO
  Easier boiler retrofit
  Less intensive capital costs
  Less visible

## Slide 28: RFO Operation
RFO will become our base fuel, coal and natural gas will be supplemental
Boilers 1 & 4
  RFO, Natural Gas and Coal Capability
  Ability to fire on RFO and Natural Gas or Coal simultaneously
  Base load of RFO to provide “Comfort Heat”
  Remaining load of coal or gas to provide “Process Heat”
Boilers 2 & 3 will have Natural Gas and Coal Capability

## Slide 29: RFO Operation
Rail Distribution to area
Off-Load and truck to Duluth Energy Systems
Multiple days of capacity in on-site storage tanks

## Slide 30: Next Steps
Permit work has begun
Need to determine what pollution control equipment is needed for RFO / Natural Gas combination
Current agreement will displace between 1/3 and ½ of current fuel requirements

## Slide 31: Strategic Plan
Lower Costs
Modern Distribution
Increased Reliability
Forward Thinking